## Slide 1
2. SIP-MRG

## Slide 2
Stronger Security for “Remote” account
SIP-MRG
Internet
PSTN
Ext 101
Port Forward
to PBX
Cracker
SIP Log-in to Ext 101
Ext 102 Panasonic KX-HDV Ext 103 Panasonic Mobile
Softphone
(from NS V5.0)
“Remote” is set for SIP extension then you can select “Panasonic SIP Phone only” to reject other SIP terminal remote connection.
Other SIP phone is rejected to connect. Model type is recognized by PBX can be disabled by SIP extension port based programming.
Notes: 2

## Slide 3
“Local” has set for SIP extension then connection from remote is restricted, even if SIP password is correct.
With old firmware for KX-NS Connection is not restricted. Voice path does not connect correctly.
However international call fee is required when Hacker made call at PBX.
Stronger Security for “Local” account
Internet
PSTN
Ext 101
Port Forward
to PBX
Cracker
SIP Log-in to Ext 101
SIP-MRG
Ext 102 Panasonic KX-HDV Ext 103 Panasonic Mobile
Softphone
(from NS V5.0)
Notes: 3

## Slide 4
Stronger Security for “Remote” account
SIP-MRG
Following IP address is treated as Local regardless of class for IP address of PBX. 10.0.0.0 - 10.255.255.255 (Class A) 172.16.0.0 - 172.31.255.255 (Class B) 192.168.0.0 - 192.168.255.255 (Class C)
PBX define location of phone by IP address.